## Slide 1
EEL 6764 Principles of Computer Architecture
Review – Assignment 1
Computer Architecture
A Quantitative Approach, Fifth Edition
Instructor: Hao Zheng
Department of Computer Science & Engineering
University of South Florida Tampa, FL 33620 Email: haozheng@usf.edu Phone: (813)974-4757 Fax: (813)974-5456

## Slide 3
1.8 You are designing a system for real-time application in which specific deadlines must be met. Finishing the computation faster gains nothing. You find that your system can execute the necessary code, in the worst case, twice as fast as necessary.
(a) how much energy do you save if you execute at the current speed and turn off the system when the computation is complete?

## Slide 4
1.8 You are designing a system for real-time application in which specific deadlines must be met. Finishing the computation faster gains nothing. You find that your system can execute the necessary code, in the worst case, twice as fast as necessary.
(b) how much energy do you save if you set the voltage and frequency to be half as much?

## Slide 5
1.9 Server farms provide enough capacity for the highest request rate. When the servers operate at 60% of their capacity, they consume 90% of max power. Servers usually operate at 60% of their capacity. The servers could be turned off, but they would take too long to restart in response to more load. A new system has been proposed that allows for a quick restart but requires 20% of max power while in this “barely alive” state
(a) how much power savings would be achieved by turning off 60% of servers?

## Slide 6
1.9 Server farms provide enough capacity for the highest request rate. When the servers operate at 60% of their capacity, they consume 90% of max power. The servers could be turned off, but they would take too long to restart in response to more load. A new system has been proposed that allows for a quick restart but requires 20% of max power while in this “barely alive” state
(b) how much power savings would be achieved by placing 60% of servers in the “barely alive” state?

## Slide 7
1.9 Server farms provide enough capacity for the highest request rate. When the servers operate at 60% of their capacity, they consume 90% of max power. The servers could be turned off, but they would take too long to restart in response to more load. A new system has been proposed that allows for a quick restart but requires 20% of max power while in this “barely alive” state
(c) how much power savings would be achieved by reducing voltage by 20% and frequency by 40%?

## Slide 8
1.9 Server farms provide enough capacity for the highest request rate. When the servers operate at 60% of their capacity, they consume 90% of max power. The servers could be turned off, but they would take too long to restart in response to more load. A new system has been proposed that allows for a quick restart but requires 20% of max power while in this “barely alive” state
(d) how much power savings would be achieved by placing 30% of servers in the “barely alive” state and 30% off?

## Slide 9
1.12 Assume we are enhancing a machine by adding encryption engine. When computing encryption, it is 20 times faster than the normal mode of execution. We define percentage of encryption as the percentage of time in the original execution that is spent performing encryption. This specialized HW increases power by 2%.
(b) With what percentage of encryption will adding encryption HW result in a speedup of 2?

## Slide 10
1.12 Assume we are enhancing a machine by adding encryption engine. When computing encryption, it is 20 times faster than the normal mode of execution. We define percentage of encryption as the percentage of time in the original execution that is spent performing encryption. This specialized HW increases power by 2%.
(c) What percentage of time in the new execution will be spent on encryption if speedup of 2 is achieved?

## Slide 11
1.12 Assume we are enhancing a machine by adding encryption engine. When computing encryption, it is 20 times faster than the normal mode of execution. We define percentage of encryption as the percentage of time in the original execution that is spent performing encryption. This specialized HW increases power by 2%.
(d) Suppose the percentage of encryption is 50%. Assume that 90% of encryption can be parallelized. What is speedup if 2 or 4 encryption HW units are added?

## Slide 12
1.14 When making changes to optimize part of a processor, it is often the case that speeding up one type of instruction comes at the cost of slowing down something else. For example, if we put in a complicated fast floating-point unit, that takes space, and something might have to be moved farther away from the middle to accommodate it, adding an extra cycle in delay to reach that unit. The basic Amdahl’s Law equation does not take into account this trade-off.

## Slide 13
  (a) If the new fast floating-point unit speeds up floating-point operations by, on average, 2x, and floating-point operations take 20% of the original program’s execution time, what is the overall speedup (ignoring the penalty to any other instructions)?

## Slide 14
  (b) Now assume that speeding up the floating-point unit slowed down data cache accesses, resulting in a 1.5x slowdown (or 2/3 speedup). Data cache accesses consume 10% of the execution time. What is the overall speedup now?

## Slide 15
  (c) After implementing the new floating-point operations, what percentage of execution time is spent on floating-point operations? What percentage is spent on data cache accesses?

## Slide 16
1.6 When parallelizing an application, the ideal speedup is speeding up by the number of processors. This is limited by two things: percentage of the application that can be parallelized and the cost of communication. Amdahl’s Law takes into account the former but not the latter.
(a) What is the speedup with N processors if 80% of the application is parallelizable, ignoring the cost of communication?

## Slide 17
1.6 When parallelizing an application, the ideal speedup is speeding up by the number of processors. This is limited by two things: percentage of the application that can be parallelized and the cost of communication. Amdahl’s Law takes into account the former but not the latter.
(b) What is the speedup with eight processors if, for every processor added, the communication overhead is 0.5% of the original execution time.