## Slide 1
EEL 6764 Principles of Computer Architecture
Review – Assignment 2
Computer Architecture
A Quantitative Approach, Fifth Edition
Instructor: Hao Zheng
Department of Computer Science & Engineering
University of South Florida Tampa, FL 33620 Email: haozheng@usf.edu Phone: (813)974-4757 Fax: (813)974-5456

## Slide 2
B.5 You are building a system around a processor with in-order execution that runs at 1.1 GHz and has a CPI of 1.35 excluding memory accesses. Loads are 20% of all instructions, and stores are 10% of all instructions. The memory system has a split L1 cache. Both the I-cache and D-cache are direct-mapped and hold 32 KB each. The I-cache has a 2% miss rate and 32-byte blocks, and the D-cache is write-through with a 5% miss rate and 16-byte blocks. There is a write buffer on the D-cache that eliminates stalls for 95% of all writes. The 512 KB write-back, unified L2 cache has 64-byte blocks and an access time of 15 ns. It is connected to the L1 cache by a 128-bit data bus that runs at 266 MHz and can transfer one 128-bit word per bus cycle. Of all memory references sent to the L2 cache in this system, 80% are satisfied without going to main memory. Also, 50% of all blocks replaced are dirty. The 128-bit-wide main memory has an access latency of 60 ns, after which any number of bus words may be transferred at the rate of one per cycle on the 128-bit-wide 133 MHz main memory bus.

## Slide 3
  a. [10] < B.2 > What is the average memory access time for instruction accesses?
  b. [10] < B.2 > What is the average memory access time for data reads?
  c. [10] < B.2 > What is the average memory access time for data writes?
  d. [10] < B.2 > What is the overall CPI, including memory accesses?