## Slide 1
EEL 6764 Principles of Computer Architecture Instruction-Level Parallelism
Computer Architecture
A Quantitative Approach, Fifth Edition
Dr Hao Zheng
Dept. of Comp Sci & Eng
U of South Florida

## Slide 2: Reading
Appendix C
Chapter 3

## Slide 3: A Simplified View of Computers
CPU
Interconnect
HD
Cache
Memory
...
DISP
KB

## Slide 4: Introduction
Design Principle – exploit parallelism
Pipelining become universal technique in 1985
  Overlaps execution of instructions
  Exploits “Instruction Level Parallelism”
There are two main approaches:
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMD processors
  Compiler-based static approaches
    Not as successful outside of scientific applications
C.1 Introduction

## Slide 5: Instruction Execution of RISC
Initial State: PC is set to point to the first instruction
For each instruction, perform the following 5 steps:
  Instruction Fetch (IF)
  Instruction Decode/Register Read (ID)
  Execution/Effective Address Calculation (EX)
  Memory Access (MEM)
  Write Back (WB)
C.1 Introduction

## Slide 6: Instruction Execution
Instruction Fetch:
  Send PC to memory, assert MemRead signal
  Instruction read out from memory
  Place instruction in IR: IR  [PC]
  Update PC to next instruction: PC  [PC] + 4
C.1 Introduction
Notes: Why is IR needed? Allow memory access and instruction execution proceed in parallel

## Slide 7: Instruction Execution
Instruction Decode:
  Instruction in IR decoded by control logic, instruction type and operands determined
  Source operand registers read from general purpose register file
C.1 Introduction
Notes: Actions:
read registers,
check equality on registers for branch instructions
computer branch target address
sign-extend immediate/displacement field
All actions performed in parallel -> higher performance, may lead to waster of energy if actions are not needed.

## Slide 8: Instruction Execution
Execute:
  ALU operates on operands prepared in previous cycle
  One of four functions depending upon opcode
  Memory Reference
    Form effective address from base register and immediate offset
    ALU Output  [A] + Imm
  Register-Register ALU Instruction
    ALU Output  [A] op [B]
  Register-Immediate ALU Instruction
    ALU Output  [A] op Imm
  Branch
    Compute branch target by adding Imm to PC
      ALU Output  [PC] + (Imm << 2)
    Evaluate the branch condition
C.1 Introduction

## Slide 9: Instruction Execution
Memory Access:
  For load instructions, read data from memory
  For store instructions, write data to memory
C.1 Introduction

## Slide 10: Instruction Execution
Write-back:
  Results written to destination register
  Results from mem read or ALU
C.1 Introduction

## Slide 11: Instruction Execution – Example
Add R3, R4, R5 ; R3[R4]+[R5]
Source registers: R4, R5 Destination register: R3
Instruction steps:
  Fetch: Fetch the instruction and increment the program counter
  Decode: Decode the instruction in IR to determine the operation to be performed (add). Read the contents of registers R4 and R5
  Execute: Compute the sum [R4] + [R5]
  Memory Access: No action, since there are no memory operands
  Write-back: Write the result into register R3
C.1 Introduction

## Slide 12: Instruction Execution – Example
Load R5, X(R7) ; R5[[R7]+X]
Source register: R7 Destination register: R5
Immediate value X is given in the instruction word
Instruction steps:
  Fetch: Fetch the instruction and increment the program counter
  Decode: Decode the instruction in IR to determine the operation to be performed (load). Read the contents of register R7
  Execute: Add the immediate value X to the contents of R7
  Memory Access: Use the sum X+[R7] as the effective address of the source operand, read the contents of that location from memory
  Write-back: Write the data received from memory into register R5
C.1 Introduction

## Slide 13: Instruction Execution – Example
Store R6, X(R8) ; Mem[X+[R8]][R6]
Source registers: R6, R8 Destination register: None
The immediate value X is given in the instruction word
Instruction steps:
  Fetch: Fetch the instruction and increment the program counter
  Decode: Decode the instruction in IR to determine the operation to be performed (store). Read the contents of registers R6 and R8.
  Execute: Compute the effective address X + [R8]
  Memory Access: Store the contents of register R6 into memory location X + [R8]
  Writeback: No action
C.1 Introduction

## Slide 14: Basic Pipeline
To improve performance, we can make circuit faster, or use …
Ideal time/instruction =
time/instruction unpipelined
# pipeline stage
C.1 Introduction

## Slide 15
Pipeline clock cycle determined by the slowest stage.
Pipeline registers add extra overhead.
C.1 Introduction
Notes: This simple version misses some key components.
Note: Reg is updated in the 1st half of ID cycle, and it is read in the 2nd half of the ID cycle. so the 1st and 4th instructions can proceed in the same cycle even with a data dependency.

## Slide 16: Ideal Pipeline and Performance
Balanced pipeline (each stage has the same delay)
Zero overhead due to clock skew and pipeline registers
Ignore pipeline fill and drain overheads
C.1 Introduction
Number of pipeline stages

## Slide 17: Pipeline Performance
Example: A program consisting of 500 instructions is executed on a 5-stage processor. How many cycles would be required to complete the program. Assume ideal overlap in case of pipelining.
Without pipelining:
  Each instruction will require 5 cycles. There will be no overlap amongst successive instructions.
  Number of cycles = 500 * 5 = 2500
With pipelining:
  Each pipeline stage will process a different instruction every cycle. First instruction will complete in 5 cycles, then one instruction will complete in every cycle, due to ideal overlap.
  Number of cycles = 5 + ((500-1)*1) = 504
Speedup for ideal pipelining = 2500/504 = 4.96
C.1 Introduction

## Slide 18: Pipeline Performance
Problem: Consider a non-pipelined processor using the 5-stage datapath with 1 ns clock cycle. Assume that due to clock skew and pipeline registers, pipelining the processor adds 0.2 ns of overhead to the clock speed. How much speedup can we expect to gain from pipelining? Assume a balanced pipeline and ignore the pipeline fill and drain overheads. (A similar ex. in the book)
Solution:
  Without pipelining: Clock period = 1 ns, CPI = 5
  With pipelining: Clock period = 1 + 0.2 = 1.2 ns, CPI = 1
C.1 Introduction

## Slide 19: Pipeline Performance
The potential increase in performance resulting from pipelining is proportional to the number of pipeline stages
However, this increase would be achieved only if
  all pipeline stages require the same time to complete, and
  there is no interruption throughout program execution
Unfortunately, this is not true
  there are times when an instruction cannot proceed from one stage to the next in every clock cycle
C.1 Introduction

## Slide 20: Pipeline Performance
Assume that Instruction Ij+1 is stalled in the decode stage for two extra cycles
This will cause Ij+2 to be stalled in the fetch stage, until Ij+1 proceeds
New instructions cannot enter the pipeline until Ij+2 proceeds past the fetch stage after cycle 5 => execution time increases by two cycles
C.1 Introduction

## Slide 21
Pipeline Hazards

## Slide 22: Dependences
Independent instructions can be executed in parallel
An instruction can depend on another in three ways
  Data dependences
  Name dependences
  Control dependences
C.2, 3.1 Pipeline hazards
Dependences limit how much parallelism can exploited
DSUB R1, R5, R6

## Slide 23: Pipeline Hazards
Hazards prevent the next instruction in the instruction stream from executing during its designated clock cycle
Three types of pipeline hazards
  Structural hazard – a situation where two (or more) instructions require the use of a given hardware resource at the same time
  Data hazard – any condition in which either the source or the destination operands of an instruction are not available, when needed in the pipeline
    Instruction processing will be delayed until operands become available
  Control hazard – a delay in the availability of an instruction or the memory address needed to fetch the instruction
C.2, 3.1 Pipeline hazards

## Slide 24: Pipeline Hazards
Hazards may require “stalling” the pipeline allowing some instructions to proceed while others are delayed
  With no additional instructions fetched
  until the conditions that caused the hazard do not exist anymore
This is called “clearing the hazard”
Stalling increases the CPI,
  reduces the speedup from pipelining
C.2, 3.1 Pipeline hazards

## Slide 25: Structural Hazards
A situation where two (or more) instructions require the use of a given hardware resource at the same time
Example: In the MIPS 5-stage pipeline, both the “IF” and “MEM” stages require memory access
In the same cycle
  A new instruction is fetched from memory in the IF stage
  A “Load” instruction reads data from memory in the MEM stage
What happens if the memory has only one read port?
C.2, 3.1 Pipeline hazards
Notes: now arch has split memory for inst and data – one case for removing structural hazrds

## Slide 26: Structural Hazards – Stalls
Instructions ahead of the stall proceed to completion
Stall delays instruction and those following it
Stall
C.2, 3.1 Pipeline hazards

## Slide 27: Structural Hazards – Cost of Stalls
Consider two pipelined processors. Suppose data references represent 40% of the instructions executed and that the ideal CPI of the pipelined processor (no structural hazard) is 1. Assume that the processor with the hazard has a clock rate that is 1.05 times higher than the hazard free processor and incurs a one cycle stall on structural hazards as in our example. Is the pipeline with or without the structural hazard faster, and by how much?
Without structural hazard: Clock period = C, CPI = 1
With structural hazard: Clock period = C/1.05, CPI = 1 + (0.4 * 1) = 1.4
(𝐸𝑥𝑒𝑐𝑢𝑡𝑖𝑜𝑛 𝑇𝑖𝑚𝑒)𝑤𝑖𝑡ℎout 𝑠𝑡𝑟𝑢𝑐𝑡𝑢𝑟𝑎𝑙 ℎ𝑎𝑧𝑎𝑟𝑑/(𝐸𝑥𝑒𝑐𝑢𝑡𝑖𝑜𝑛 𝑡𝑖𝑚𝑒)𝑤𝑖𝑡ℎ 𝑠𝑡𝑟𝑢𝑐𝑡𝑢𝑟𝑎𝑙 ℎ𝑎𝑧𝑎𝑟𝑑= 𝐶 ∗1/((𝐶/1.05)∗1.4) = 1.05/1.4 = 0.75
  Processor without the structural hazard is faster
C.2, 3.1 Pipeline hazards

## Slide 28: How to Reduce Structural Hazards
Key Idea: Add more hardware resources
How to avoid structural hazard on memory access during IF and MEM stages?
  Separate instruction and data caches
How to avoid structural hazard on register access during ID and WB stages?
  Dual ported register file
  Write early in WB stage + Read late in ID stage
Why no structural hazard on ALU during IF (PC  PC + 4) and MEM stages?
  PC + 4 in IF stage uses a dedicated adder, not the ALU
C.2, 3.1 Pipeline hazards

## Slide 29: Data Hazards
Any condition in which either the source or the destination operands of an instruction are not available, when needed in the pipeline
Example
    add R2, R3, #100 ; R2 <- [R3] + 100
    sub R9, R2, #30 ; R9 <- [R2] + 30
  First instruction writes to register R2 in the WB stage
  Second instruction reads register R2 in the ID stage
  If second instruction reads R2 before the first instruction writes R2, the result of second instruction would be incorrect, as it would be based on R2’s old value (read-after-write dependence)
  To obtain the correct result, second instruction needs to wait until the first instruction has written to R2
C.2, 3.1 Pipeline hazards

## Slide 30: Data Hazards
sub is stalled in decode stage for two additional cycles to delay reading R2 until the new value of R2 has been written by add
Control circuitry recognizes the data dependency when it decodes sub (comparing source register ids with dest. register ids of prior instructions)
During cycles 3 to 5:
  add proceeds through the pipe
  sub is held in the ID stage
In cycle 5
  add writes R2 in the first half cycle, sub reads R2 in the second half cycle
C.2, 3.1 Pipeline hazards
sub R9, R2, #30
add R2, R3, #100

## Slide 31: Types of Data Hazards
Read After Write (RAW) <-- True dependence
  Caused by “dependence”. Subsequent instruction has actual need for data produced by earlier instruction
Write after Read (WAR) <-- False dependence
  Called “anti-dependence”. Can’t occur in in-order pipelines (e.g., our simple MIPS pipeline). We’ll see it later in advanced pipelines
Write after Write (WAW) <-- False dependence
  Called “output dependence”. Can’t occur in in-order pipelines (e.g., our simple MIPS pipeline). We’ll see it later in advanced pipelines
C.2, 3.1 Pipeline hazards

## Slide 32: Types of Data Hazards - RAW
Instj tries to read operand before Insti write it (j > i)
This hazard results from a true dependence: data flow from instruction i to instruction j
    Instr i: add r1, r2, r3
    Instr j: sub r4, r1, r3
C.2, 3.1 Pipeline hazards

## Slide 33: Types of Data Hazards - WAR
Instj tries to write operand before Insti reads it (j > i)
This is an anti-dependence (not a true dependence)
  Arises from the reuse of register “r1”
  If Instr i writes to r1 before Instr j reads r1, then Instr i will use the value written by Instr j => Incorrect behavior
WAR hazards cannot happen in MIPS 5-stage pipeline:
  Instructions are executed in order
  Register reads happen earlier (stage-2) than register writes (stage-5)
    Instr i: sub r4, r1, r3
    Instr j: add r1, r2, r3
C.2, 3.1 Pipeline hazards

## Slide 34: Types of Data Hazards - WAW
Instrj writes to operand before Instri writes to it (j > i)
    Instr i: sub r1, r4, r3
    Instr j: add r1, r2, r3
    Instr k: mul r6, r1, r7
This is an output dependence (not a true dependence)
  Arises from the reuse of register r1
  If Instrj writes to r1 before Instri then Instrk will use the value written by Instri => violation of program order
WAW hazards cannot happen in MIPS 5-stage pipeline because:
  Instructions are executed in order
  Register writes are always in stage-5
C.2, 3.1 Pipeline hazards

## Slide 35: Data Hazards – Stall Penalty
If the dependent instruction follows right after the producer instruction, we need to stall the pipe for 2 cycles
Stall penalty = 2
sub R9, R2, #30
add R2, R3, #100
C.2, 3.1 Pipeline hazards

## Slide 36: Data Hazards – Stall Penalty
What happens if the producer and dependent instructions are separated by an intermediate instruction?
In this case, stall penalty = 1
Stall penalty depends upon the distance between the producer and dependent instruction
sub R9, R2, #30
add R2, R3, #100
or R4, R5, R6
C.2, 3.1 Pipeline hazards

## Slide 37: Data Hazards – Stall Penalty
Frequent stalls caused by data hazards can impact the performance significantly.
Example: If every 5 instructions have 2 stall cycles due to a data hazard, then the CPI can increase by (1/5)*2 = 0.4 stall cycles
Would like to avoid stalls caused by RAW hazards
  Technique: forwarding
Also called “bypassing” or “short-circuiting”
  Key Idea: Forward results from later stages in the pipeline to earlier stages
  i.e. Move data to where it is needed when it becomes available
C.2, 3.1 Pipeline hazards

## Slide 38: Reduce Data Hazard Stalls – Forwarding
Consider the two instructions discussed in the previous example
  The result of producer instruction is actually available after the completion of EX stage (cycle 3), when the ALU completes its computation
  Instead of stalling the dependent instruction, the hardware can forward the result from the output of the EX stage to the ALU, where it can be used by the dependent instruction
  The arrow in below figure shows data being forwarded from EX stage of first instruction to EX stage of the second instruction
add R2, R3, #100
sub R9, R2, #30
C.2, 3.1 Pipeline hazards
Notes: sources of data that are needed by a following instruction: output of EX or MEM

## Slide 39: Pipeline Hazards – An Example
C.2, 3.1 Pipeline hazards

## Slide 40: Reduce Data Hazard Stalls – Forwarding
C.2, 3.1 Pipeline hazards

## Slide 41: Reduce Data Hazard Stalls – Forwarding
Passing results from one stage to inputs of another stage
C.2, 3.1 Pipeline hazards

## Slide 42: Data Hazard Requiring Stalls
C.2, 3.1 Pipeline hazards

## Slide 43
Branch Hazards

## Slide 44: Branch Hazards
Control hazards are caused by a delay in the availability of an instruction or the memory address needed to fetch the instruction
In ideal pipelined execution, a new instruction is fetched every cycle, while the previous instruction is being decoded
This will work fine as long as the instruction addresses follow a pre-determined sequence (e.g., PC [PC]+4)
However, branch instructions can alter this sequence
Branch instructions first need to be executed to determine whether and where to branch
Pipeline needs to be stalled before the branch outcome is decided
C.2, 3.1 Pipeline hazards

## Slide 45: Conditional Branches – 1
Consider a conditional branch instruction such as
Testing the branch condition (comparison between [R5] and [R6]) determines whether the branch is taken or not taken
  also, compute branch target address PC + loop
loop: ld R1, 0(R6)
...
BEQ R5, R6, loop
add R2, R4, R5
C.2, 3.1 Pipeline hazards
Notes: define “taken” and “non taken”

## Slide 46: Conditional Branches – 2
Both the comparison and target address calculation happens in the EX stage (3rd cycle of instruction processing)
If the branch is taken
  Cannot fetch the branch target before the start of 4th cycle
  No useful instruction fetched in cycles 2 and 3 Control Hazard
  Stall penalty = 2 cycles
C.2, 3.1 Pipeline hazards

## Slide 47: Handling Control Hazards
Let us assume R5 = R6
In cycle-3, EX stage determines that the branch is taken and computes the target address
PC is updated with the branch target address
Two instructions (Ij+1 and Ij+2) on the wrong path have already been fetched
C.2, 3.1 Pipeline hazards

## Slide 48: Handling Control Hazards
Control transfers to branch target (Ik)
Instructions Ij+1 and Ij+2 flushed from the pipeline
Branch Penalty in this case is 2 cycles
What would be the Branch Penalty if the branch was not taken?
C.2, 3.1 Pipeline hazards

## Slide 49: Reduce Branch Penalty
How to reduce the branch penalty for conditional branches?
  Test the branch condition in the ID stage
    Move the comparator from EX stage to ID stage
    Branch condition tested in parallel with target address computation
    Branch penalty reduced to one cycle
  Also compute the branch target address in the ID stage
    Need an adder in the ID stage to add the branch offset to the PC
    When the decoder determines that the instruction is a conditional branch, the computed target address is available before the end of the ID stage
    Update the PC before the end of ID stage
  Negative Effect: ID stage lengthened; may have to increase the clock period
C.2, 3.1 Pipeline hazards

## Slide 50: Reduce Branch Penalty
Branch condition and target address computed in cycle # 2
Branch penalty reduced to one cycle
Only one instruction (Ij+1) is fetched incorrectly and needs to be discarded
C.2, 3.1 Pipeline hazards

## Slide 51: Reducing Pipeline Branch Penalties – 1
Pipeline flush – simple, but w. fixed branch penalties
  Stall until branch target is known
Predicted-not-taken
  Increment PC by 4 every cycle and keep fetching sequential instructions after the branch instruction
  After the branch outcome is computed
    If the branch condition is false (Not-taken branch):
      We have already been fetching instructions from the correct path => no problem
    But if the branch condition is true (Taken branch):
      Need to start fetching from the branch target
      What happens to the instructions that have already been fetched on the wrong path?
C.2, 3.1 Pipeline hazards

## Slide 52: Reducing Pipeline Branch Penalties – 2
Predicted-not-taken
C.2, 3.1 Pipeline hazards

## Slide 53: Handling Control Hazards
Predict-taken: Treat every “branch” as taken
  In our 5-stage pipeline, we don’t know target any earlier than we know branch outcome
  No advantage, unless we could predict the target address earlier in the pipeline
Delayed Branch
  Compiler optimization
  Use knowledge of the program semantics to rearrange instructions before/after the branch
C.2, 3.1 Pipeline hazards

## Slide 54: Delayed Branch
Branch instruction
Sequential successor - in branch delay slot
Branch target if taken
C.2, 3.1 Pipeline hazards

## Slide 55: Scheduling Branch Delay Slot
C.2, 3.1 Pipeline hazards

## Slide 56: Example
SD R7, 0(R8)
BEQ R5, R6, IF
LD R2, 16(R1)
DADD R3, R4, R2
IF: LD R2, 64(R1)
DSUB R3, R4, R2
Branch hazards?
Data hazards?
Suppose that branch penalty is 1 cycle.
C.2, 3.1 Pipeline hazards

## Slide 57: Performance of Branch Schemes
C.2, 3.1 Pipeline hazards

## Slide 58: Performance of Branch Schemes - Example
Assume that branches comprise 20% of all instructions. Also assume that the branch prediction is 80% accurate and incurs a 2 cycle stall on each misprediction. What is the impact of control hazards on the CPI of the pipelined processor? Ignore all other sources of pipeline hazards.
-------------------------------------------------------------------------
CPI without control hazards = 1
Added CPI due to control hazards = Branch frequency * (1 – Branch prediction accuracy) * Stall penalty = 20% * (1 - 80%) * 2 = 0.08
CPI with control hazards = 1 + 0.08 = 1.08
C.2, 3.1 Pipeline hazards

## Slide 59: Another Example
Speedup of “predicted-not-taken” over “stall pipeline” = 1.56 / 1.38 = 1.13
C.2, 3.1 Pipeline hazards

## Slide 60: Branch Prediction
Static Prediction
  Individual branches biased toward taken or not-taken
  Based on profile information
  Limited by: high misprediction rate + high branch frequency
Dynamic Prediction
  1 bit predictor - remember last taken/not taken per branch
  Use a branch-prediction buffer or branch-history table with 1 bit entry
  Use part of the PC (low-order bits) to index buffer/table –Why?
    Multiple branches may share the same bit
  Invert the bit if the prediction is wrong
  Backward branches for loops will be mis-predicted twice
    Once upon loop exit and then again on loop entry
C.2, 3.1 Pipeline hazards
Notes: Hypothesis: a branch (taken or not-taken) will likely repeat the same decision next time.
This is true for branches involved in loops.

## Slide 61: 1-Bit Predictor
BHT: Branch Prediction Buffer in textbook
Use only one 1-bit predictor
  accuracy is low
BHT: use a table of simple predictors, indexed by bits from PC
  Similar to direct mapped cache
  More entries, more cost, but less conflicts, higher accuracy
  BHT can contain complex predictors
T
Predict Taken
Predict Not Taken
T
NT
T
NT
NT
Prediction
K-bit
Branch
address
2k
What about PCs of two branches having the same lower bits?
C.2, 3.1 Pipeline hazards

## Slide 62: 1-Bit Predictor
Example: in a loop, 1-bit BHT will cause 2 mis-predictions
Consider a loop of 9 iterations before exit:
  for (…){
  for (i=0; i<9; i++)
  a[i] = a[i] * 2.0;
  }
  End of loop case, when it exits instead of looping as before
  First time through loop on next time through code, when it predicts exit instead of looping
  Mis-predict twice every time the inner loop is executed
C.2, 3.1 Pipeline hazards

## Slide 63: 2-Bit Predictor
Solution: 2-bit scheme where change prediction only if get mis-prediction twice consecutively
Other solutions: correlating predictor, tournament predictors
C.2, 3.1 Pipeline hazards

## Slide 64: 2-Bit Predictor Accuracy
BHT: 4096 entry 2-bit buffer
C.2, 3.1 Pipeline hazards

## Slide 65: 4K vs Unlimited Buffer for Prediction
C.2, 3.1 Pipeline hazards

## Slide 66: Correlating Branch Predictors
Rationale: branch outcomes may be correlated
If (aa == 2)
aa = 0;
If (bb == 2)
bb = 0;
If (aa != bb) {…}
If both b1 and b2 are not taken, then b3 is taken.
Use history of last m branches to predict the current one.
3.3 Advanced Branch Prediction
addi x3,x1,–2
bnez x3,L1 //branch b1 (aa!=2)
add x1,x0,x0 //aa=0
L1: addi x3,x2,–2
bnez x3,L2 //branch b2 (bb!=2)
add x2,x0,x0 //bb=0
L2: sub x3,x1,x2 //x3=aa-bb
beqz x3,L3 //branch b3 (aa==bb)
Notes: branch b3 is correlated to b1 and b2.

## Slide 67: Correlating Branch Predictors
Use history of last m branches to predict the current branch.
  Each predictor uses n bits.
Global history register
of last m branches
t
t
nt
t
nt
t – taken
nt – not taken
Shift register
Branch prediction buffer
(2m entries, each of n-bits)
3.3 Advanced Branch Prediction
Notes: Benefit: higher prediction accuracy, low HW overhead.

## Slide 68: Correlating Branch Predictors
Use history of last m branches to predict the current branch.
  Each predictor uses n bits.
Global history register
of last m branches
t
t
nt
t
Shift register
Branch prediction buffer
(2m+k entries, each of n-bits)
Low order k-bits
of branch address
m+k
3.3 Advanced Branch Prediction
nt

## Slide 69: Correlating Branch Predictors
Tournament predictor selects the best of local and global predictors, and leads to better prediction.
3.3 Advanced Branch Prediction

## Slide 70
Pipeline Implementation

## Slide 71: Non-Pipelined Version
C.3 Pipeline Implementation

## Slide 72: A Basic MIPS Pipeline
Temporary registers become part of PL registers.
PL registers carry partial results from one stage to the next.
C.3 Pipeline Implementation

## Slide 73: A Basic MIPS Pipeline
C.3 Pipeline Implementation

## Slide 74: A Basic MIPS Pipeline
C.3 Pipeline Implementation

## Slide 75: A Basic MIPS Pipeline
C.3 Pipeline Implementation

## Slide 76: A Basic MIPS Pipeline
C.3 Pipeline Implementation

## Slide 77: Hazard Detection
Instruction issue: move from ID to EX.
Detect data hazards during ID
  Stall the instruction before it is issued
  Insert pipeline bubbles (no-­ops) by changing control fields to 0s
  (DADD R0, R0, R0)
Early detection of interlocks (e.g., due to a load) reduces complexity
Detect interlock by comparing:
  Source registers in IF/ID (consumers) with
  Destination register in ID/EX or EX/MEM (producer)
C.3 Pipeline Implementation

## Slide 78: Hazard Detection – Example
C.3 Pipeline Implementation

## Slide 79: RISC-V Instruction Formats
A.9 RISC-V Architecture

## Slide 80: Hazard Detection – Example
All instruction combinations are considered
Upon detection of a hazard,
  ID/EX is flushed  bubble
  IF/ID remains unchanged
6
C.3 Pipeline Implementation

## Slide 81: Forwarding
C.3 Pipeline Implementation
Notes: 3 new inputs to ALU, ALUOutput at the end of EX and MEM stages, and MemOutput at the end of MEM stage.

## Slide 82: Forwarding
Sources: outputs of
  ALU or Memory
Destinations: inputs of
  ALU, Memory, Branch decision
Forwarding done by controlling MUXs of the inputs at destinations
Compare registers in EX/MEM or MEM/WB with registers in ID/EX and EX/MEM.
Ex:
ld R1, 45(R2)
add ...
sub R8, R1, R7
MEM/WB.IR[rd] == ID/EX.IR[rs1]
controls an input MUX to ALU.
C.3 Pipeline Implementation
Notes: 3 new inputs to ALU, ALUOutput at the end of EX and MEM stages, and MemOutput at the end of MEM stage.

## Slide 83: Branches in Pipeline
C.3 Pipeline Implementation

## Slide 84: Branches in Pipeline
C.3 Pipeline Implementation
BEQZ Rx, name ; if (Regs[Rx]==0) PC <- name
Notes: In older MIPS, branch condition test is moved to ID if such test is restricted like test ”=0?”.
More complex test requires more complex logic, thus adding delay to ID  longer cycle time.

## Slide 85: Extend Pipeline to Handle Long Latency
Impractical to require all FP operations to complete in 1 cycle
  Longer cycle time
  Large area overhead
Long FP operations
  take multiple cycles
Non-pipelined
  Stalls caused by long latency FP operations
C.5 Multicycle Operations

## Slide 86: Extend Pipeline to Handle Long Latency
Pipelining functional units allow multiple instructions to be executed.
C.5 Multicycle Operations

## Slide 87: Extend Pipeline to Handle Long Latency
Latency: number of cycles between two dependent instructions.
Interval: number of cycles between two consecutive instructions of the same type.
C.5 Multicycle Operations

## Slide 88: Extend Pipeline to Handle Long Latency
Structural hazards can occur due to long latency
Simultaneous register writes are possible
  due to various execution latencies
WAW hazards are now possible
Instructions can complete in different orders
C.5 Multicycle Operations

## Slide 89: Extend Pipeline to Handle Long Latency
Long latency causes more stalls for RAW hazards
C.5 Multicycle Operations