## Slide 1
EEL 6764 Principles of Computer Architecture Final Review
Computer Architecture
A Quantitative Approach, Fifth Edition
Dr Hao Zheng
Dept. of Comp Sci & Eng
U of South Florida

## Slide 2: Computer Architecture – Big Picture
uP
Interconnect
HD
DISP
KB
Cache
Memory
...

## Slide 3: ISA Design
Different architectures
  Classified by organizations of operands -- stack, accumulator, GP registers
  Classified by granularity – CISC vs RISC
Objectives: performance, implementability, compatibility
Considerations
  Number of registers
  Number of operands
  Memory addressing mode
  Types of instructions
  Instruction encoding – fixed vs flexible
    impact of code size

## Slide 4: ILP and Pipelining
ILP – overlapped executions of different instructions
Pipelining – architecture to exploit ILP
Architecture of 5-stage MIPS pipeline
  IF, ID, EX, MEM, WB
Ideal pipeline performance
  Speedup is close to number of pipeline stages
  Pipeline hazards, mem & FU latency, pipeline register delays
Pipeline hazards
  Structural – a hardware issue
  Data – dependencies in programs
  Control - related to branches

## Slide 5: ILP and Pipelining
Hazard handling – stall (simple, but undesirable)
  Structural – replicate HW, or pipelining slow components
  Data – RAW, WAR, WAW
    forwarding for RAW, register renaming for WAR & WAW
  Branch
    Branch prediction -- static & dynamic, 1-bit & 2-bit predictors
    HW speculation

## Slide 6: ILP and Pipelining
Scheduling – what is it?
  Static vs dynamic – issues of static scheduling
  register renaming – WAW & WAR hazards
  Tomasulo’s algorithm
    reg renaming + dynamic scheduling
    reservation stations, CDB, tags for registers
    operations – see Figure 3.13.
HW speculation – what is it, and how does it work?
  What problem does it solve?
  What additional HW is used and operated? (see Fig. 3.18)
  Efficiency depends on branch prediction accuracy

## Slide 7: ILP and Pipelining
Multi-Issue
  Goal: reduce CPI to <1
  Challenge – complexity of issue logic (see Fig 3.22)
Multithreading – target thread-level parallelism
  Fine-grained
  Coarse-grained
  Simultaneous multithreading – additional PCs and registers

## Slide 8: Memory Hierarchy Design
  Mem latency – limiting factor of performance
  Cache – Reduce average memory access latency
  spatial & temporal locality
  Organization
  Set Associativity
  Cache misses, and their causes
  Performance measurement
  Write policy – write-back vs write-through
  Optimization techniques
Virtual memory – memory as cache for hard disk
  Roles: memory management and protection
  Organization: page, page table, page faults; addr translation
  TLB – cache for page table

## Slide 9: TLP and Multiprocessors
Parallel execution of instructions from different threads
Multiprocessor = a set of processors connected together
  Support MIMD execution model
Multiprocessing vs multithreading
Architectures
  Symmetric MP, aka, centralized shared memory MP
  Distributed shared memory MP
  Coordination – shared memory
  Caching – reduce remote memory access latency
  Introduce coherence problem
  Cache Coherence protocols – snooping vs directory
    Write-invalidate vs write-update

## Slide 10: Vector Processors
DLP – parallel operations on different data
Vector architecture
  Exploit DLP
  Support SIMD execution model
Target applications with many vector operations/loops
Main architecture features
  Vector registers,
  Vector load/store unit, addressing with stride, gather-scatter
  Pipelined functional units, multiple lanes, chaining
  Vector length register, strip mining
  Vector predicate register for conditional execution over vectors
Differences against superscalar processors