## Slide 1
EEL 6764 Principles of Computer Architecture
Data-Level Parallelism in Vector, SIMD and GPU Architectures
Computer Architecture
A Quantitative Approach, Fifth Edition
Dr Hao Zheng
Dept of Comp Sci & Eng
U of South Florida

## Slide 2: Flynn’s Classification
4.1 Introduction
 | Single Data | Multiple Data
Single Instruction | SISD | SIMD
Multiple Instructions | Not Exists | MIMD
Notes: getting more important as more data-driven applications are popping up

## Slide 3: Data Parallelism
Concurrency arises from performing the same operations on different pieces of data
  Single instruction multiple data (SIMD)
  E.g., dot product of two vectors
Contrast with data flow
  Concurrency arises from executing different operations in parallel (in a data driven manner)
Contrast with thread (“control”) parallelism
  Concurrency arises from executing different threads of control in parallel
4.1 Introduction

## Slide 4: Introduction
SIMD architectures can exploit significant data-level parallelism for:
  matrix-oriented scientific computing
  media-oriented image and sound processing
SIMD is more energy efficient than MIMD
  Fetch one instruction for many data operation
  Makes SIMD attractive for personal mobile devices
SIMD allows programmer to continue to think sequentially
  Unlike MIMD
4.1 Introduction

## Slide 5: SIMD Processing
Single instruction operates on multiple data elements
  In time – PEs are pipelined
  In space – Multiples PEs
Time-Space Duality
  Array processor – instruction operates on multiple data at the same time, needs duplicates of PEs
  Vector processor – instruction operates on multiple data in consecutive time steps, PEs needs to be pipelined
4.1 Introduction

## Slide 6: Vector Architecture
A vector is a one-dimensional array of numbers
  Many scientific/commercial applications use vector
An instruction operates on vectors, instead of scalar values
  Each instruction generates a lot of work
Basic idea:
  Read vectors of data elements into vector registers
  Vector FUs operate on those registers in a pipelined manner one element at a time
  Disperse the results back into memory
4.1 Introduction

## Slide 7: Vector Architecture
FUs are deeply pipelined
  No intra-vector dependence – no HW interlocking within a vector
  No control-flow within a vector
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Deliver high performance without energy/design complexity of out-of-order superscalar processor
  Increase performance of in-order simple scalar
4.1 Introduction

## Slide 8: RISC-V Vector Architecture
Memory
      Each register holds a 64-element, 64 bits/element vector
      Register file has 16 read ports and 8 write ports
      Other special purpose registers, i.e VLR/MVL.
4.2 Vector Architecture
Notes: large number of register ports support operations on different registers in parallel.

## Slide 9: RISC-V Vector Architecture
Memory
4.2 Vector Architecture
      Fully pipelined – start a new op on every cycle
      Control unit detects data & structural hazards
Notes: data hazards on accessing registers
structural hazards on FUs

## Slide 10: Vector Functional Units
      Use deep pipeline to execute elements at fast speed
      No intra-vector dependence leads to simple pipeline control
4.2 Vector Architecture

## Slide 11: RISC-V Vector Architecture
Memory
      Fully pipelined – one word to/from memory per cycle after initial latency
      Also handle scalar load/store
Memory needs to have high bandwidth to support vector load/store
4.2 Vector Architecture
Notes: pipelined load/store hides mem access latency by amortizing it over large number of consecutive accesses.

## Slide 12: RISC-V Vector Architecture
Memory
      32 GP registers
      32 FP registers
4.2 Vector Architecture

## Slide 13: RISC-V Vector Instructions
vadd: add two vectors
vld/vst: vector load and vector store from address
Example: DAXPY – Y = a * X + Y ; vector length = 64
Requires 6 instructions vs. almost 600 for MIPS
vsetdcfg 4*FP64 # Enable 4 DP FP vregs
fld f0, a # Load scalar a
vld v0, x5 # Load vector X
vmul v1, v0, f0 # Vector-scalar mult
vld v2, x6 # Load vector Y
vadd v3, v1, v2 # Vector-vector add
vst v3, x6 # Store the sum
vdisable # Disable vector regs
4.2 Vector Architecture

## Slide 14: VMIPS Vector Instructions
Example: DAXPY – Y = a * X + Y
Almost 600 MIPS instructions
fld f0, a # Load scalar a
addi x28, x5, 256 # Last address to load
Loop: fld f1,0(x5) # Load X[i]
fmul.d f1, f1, f0 # a × X[i]
fld f2, 0(x6) # Load Y[i]
fadd.d f2, f2, f1 # a × X[i] + Y[i]
fsd f2, 0(x6) # Store into Y[i]
addi x5, x5, 8 # Increment index to X
addi x6, x6, 8 # Increment index to Y
bne x28, x5, Loop # Check if done
4.2 Vector Architecture
Notes: stalls between MUL and ADD happen on every data operation in superscalar
Only one stall for all 64 operations in vector machine

## Slide 15: Vector Chaining – Handling D-Dependence
Vector version of forwarding
Next vector operation starts when the result from previous operation on the 1st element is finished.
4.2 Vector Architecture

## Slide 16: Vector Chaining
Without chaining
With Chaining
4.2 Vector Architecture
Notes: * With chaining, dependent instruction can start as soon as first result appears

## Slide 17: Multiple Lanes
How can a vector processor execute a single vector faster than one element in a clock cycle?
Lane: one copy of FU + a portion of vector register file
4.2 Vector Architecture

## Slide 18: Multiple Lanes
Goal: Execute >1 element per cycle.
Use multiple FUs to improve performance of a single vector add operation C = A + B
Elements are interleaved across FUs
Increase performance to 4 elements per cycle from 1 per cycle
A[1]
B[1]
A[3]
B[3]
4.2 Vector Architecture

## Slide 19: Multiple Lanes
Element n of vector register A is “hardwired” to element n of vector register B
Each lane handles a portion of vector registers
Both applications and HW architecture must support long vectors to take advantage of the higher processing power of multiple lanes
Increase performance with the same power – by reducing clock rate by half, and doubling lanes
4.2 Vector Architecture
Notes: each lane = a portion of register file + one instance of every vector FU
Every lane computes one element / clock cycle

## Slide 20: Vector Length Register (VLR)
What if n is not know at compile time, but may be larger than the maximal vector length (MVL)?
for (i=0; i < n; i = i + 1)
Y[i] = a * X[i] + Y[i]
Known only at runtime
VLR controls the length of every vector operation
Set by setvl
What if vector length is different from the length of vector registers? Or
The length is known only at runtime?
4.2 Vector Architecture

## Slide 21: Strip Mining
for (i=0; i < n; i = i + 1)
Y[i] = a * X[i] + Y[i]
  low = 0;
  VL = (n % MVL); /*find odd-size piece using modulo op % */
  for (j = 0; j <= (n/MVL); j=j+1) { /*outer loop*/
  for (i = low; i < (low+VL); i=i+1) /*runs for length VL*/
  Y[i] = a * X[i] + Y[i] ; /*main operation*/
  low = low + VL; /*start of next vector*/
  VL = MVL; /*reset the length to maximum vector length*/
  }
4.2 Vector Architecture
Notes: convert a loop to 2 loops: one with iterations that are multiple of MVL, and one with the remaining iterations of original loop

## Slide 22: Predicate Register
  for (i = 0; i < 64; i=i+1)
  if (X[i] != 0)
  X[i] = X[i] - Y[i] ;
  IF statement introduces control dependence, reduces the level of parallelism
vsetdcfg 2*FP64 # Enable 2 64b FP vector regs
vsetpcfgi 1 # Enable 1 predicate register
vld v0,x5 # Load vector X into v0
vld v1,x6 # Load vector Y into v1
fmv.d.x f0,x0 # Put (FP) zero into f0
vpne p0,v0,f0 # Set p0(i) to 1 if v0(i)!=f0
vsub v0,v0,v1 # Subtract under vector mask
vst v0,x5 # Store the result in X
vdisable # Disable vector registers
vpdisable # Disable predicate registers
4.2 Vector Architecture
Notes: controls insides loops prevent vectorization

## Slide 23: Predicate Register
4.2 Vector Architecture

## Slide 24: Memory Banks
Memory system must be designed to support high bandwidth for vector loads and stores
Spread accesses across multiple banks
  Control bank addresses independently
  Load or store non sequential words
  Support multiple vector processors sharing the same memory
4.2 Vector Architecture
Notes: memory needs to supply enough data to keep FUs busy

## Slide 25: Memory Banks – Example
Question: A vector machine has 32 processors, each can generate 4 loads and 2 stores per cycle. SRAM cycle time is 7 cycles. What is the minimum number of memory banks needed to allow all processors to run at full bandwidth?
Answer: the max number of memory references per cycle is 32*6 = 192.
The min number of memory banks is 192*7 = 1344.
4.2 Vector Architecture

## Slide 26: Vector Stride – Handling Multi-D Arrays
4.2 Vector Architecture
How are matrices stored in memory?
Assume all A, B, D are 100x100 matrices

## Slide 27: Memory Layout of Matrices
4.2 Vector Architecture
Row-major
Consider M[i][j]
M[0][0]
M[0][1]
...
M[0][j-1]
M[1][0]
...
M[1][j-1]
M[2][0]
...
M[2][j-1]
...
M[0][0]
M[1][0]
...
M[i-1][0]
M[0][1]
...
M[i-1][1]
M[0][2]
...
M[i-1][2]
...
Column-major
Notes: elements in rows or columns are not adjacent in memory

## Slide 28: Vector Stride
4.2 Vector Architecture
Stride = distance that separate elements in a array to be gathered into a single register.
For D, in row-major layout, the stride is 100 double words, or 800 bytes
Assume all A, B, D are 100x100 matrices

## Slide 29: Vector Stride
Vector base address and stride are stored in GP registers
  Use vlds/vsts for memory access with strides
Memory bank conflicts due to Mem access with stride
  Stall memory accesses
4.2 Vector Architecture
Question: 8 Mem banks, with busy time of 6 cycles for each bank. Mem latency is 12 cycles. Time to access 64 data with stride of 1 and 32?
Answer: When stride = 1, access time = 12 + 64 = 76 cycles.
When stride = 32, access time = 12 + 1 + 6*63 = 391 cycles

## Slide 30: Gather and Scatter
Sparse matrices are arrays where most elements are 0
Sparse matrices are stored in a compact format, and accessed indirectly.
A and C have the same number of non-zero elements
  Index vectors are K and M are the same size.
4.2 Vector Architecture
1 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 6

## Slide 31: Gather and Scatter
Access sparse matrices using index vectors.
Gather load takes an index vector and fetches vector elements whose addresses are base + offset
  Offsets are stored in the index vector
Scatter store values in vector registers to Mem addresses computed as above.
Allows sparse matrix operations to run in vector mode
4.2 Vector Architecture

## Slide 32
Graphics Processing Units

## Slide 33: CUDA Architecture
4.4 Graphics Processing Units

## Slide 34: Stream Multiprocessor
4.4 Graphics Processing Units

## Slide 35: Thread Execution
4.4 Graphics Processing Units

## Slide 36: Thread Execution
4.4 Graphics Processing Units

## Slide 37
4.4 Graphics Processing Units

## Slide 38: Programming Model
4.4 Graphics Processing Units

## Slide 39: Programming Model
4.4 Graphics Processing Units
GPU executes grids of threads
A stream multiprocessor executes one or more thread blocks
A CUDA core executes threads

## Slide 40: Vector vs GPU
4.4 Graphics Processing Units

## Slide 41: Vector vs GPU
Vector:
  no multithreading
  hide mem latency by deep pipelining
GPU:
  stream multiprocessors --> multithreading
  hide mem latency by multithreading
4.4 Graphics Processing Units

## Slide 42: CPU vs GPU
CPU: low latency, low throughput
  Cache, out-of-order execution, speculation, ...
GPU: high latency, high throughput

## Slide 43: CPU vs GPU - Parallelism
CPU: task/instruction parallelism
  Multiple tasks map to multiple threads
  tasks run different instructions
  10s of relatively heavyweight threads run on 1-s of cores
  each thread managed and scheduled explicitly
  each thread individually programmed
GPU: data parallelism
  SIMD execution model
  same instruction operates on different data
  10,000s of lightweight threads on 100s of cores
  threads managed and scheduled by hardware
  programming done for batches of threads (program on vectors of data)

## Slide 44
Backup

## Slide 45: Vector Instruction Parallelism
Can overlap execution of multiple instructions
4.2 Vector Architecture
A[i] = B[i] * C[i]

## Slide 46: Vector Chaining
Vector version of register bypassing
  First appeared in Cray-1
4.2 Vector Architecture

## Slide 47: Vector Chaining
4.2 Vector Architecture
Without chaining, an dependent instruction must wait for the results from a previous instruction to be written into register
With chaining, an dependent instruction can start as soon as results from a previous instruction become available

## Slide 48: Loop Vectorization
4.2 Vector Architecture