## Slide 1: Overview of HW/SW Co-Design (Chapter 1, The CoDesign Book)
Hao Zheng
Comp Sci & Eng
U of South Florida

## Slide 2: Hardware/Software Co-Design
Definition: HW/SW co-design is the design of cooperating HW components and SW components in a single design effort.
Alternative definition:
HW/SW co-design means meeting system level objectives by exploiting the synergy of HW and SW through concurrent design.

## Slide 3: HW: Characterization
A single-clock synchronous digital circuit.
  Or an equivalent cycle-accurate model
A simplified view
  Events within a clock cycle cannot be captured.

## Slide 4: SW: Characterization
A single-thread sequential program
  In C or assembly languages.
C programs are useful to describe computations.

## Slide 5: HW and SW in a System Design
HW/SW co-design is the partitioning and design of an application in terms of fixed and flexible components.

## Slide 6: Natures of HW & SW
To implement an application: choose HW or SW?

## Slide 7: Compare HW & SW: Performance
CoDesign book

## Slide 8: Compare HW & SW: Performance
HW implementation (ASIC) has higher performance over SW running on processors.
However, processors may have a much higher clock frequency.
  the speed advantage of ASICs over software is not clear.
Therefore, absolute performance is not a very good metric to compare hardware and software

## Slide 9: Compare HW & SW: Energy Efficency
Energy efficiency: the amount of useful work done per unit of energy
the energy consumption of an AES engine (encryption) on different archi- tectures.

## Slide 10: Compare HW & SW: Summary
There is a large overhead associated with executing software instructions in the processor implementation
  Instruction and operand fetch from memory
  Complex state machine for control of the datapath, etc.
Flexibility comes with a significant energy cost
  One which energy optimized applications cannot tolerate
Therefore, you will never find a Pentium processor in a cell phone!
Specialized hardware architectures are usually also more efficient than software from a relative perspective.
  Relative performance means the amount of useful work done per clock cycle.

## Slide 11: Driving Factors in HW/SW Co-Design
Fig. 1.6 Driving Factors in hardware/software codesign
CoDesign book

## Slide 12: HW/SW Co-Design Space
related to design
methodologies

## Slide 13: Platform Selection
General-purpose platforms, such as processors or FPGAs, can support a wide range of applications.
Application-specific platforms, such as ASICs, are optimized for a single application
In the middle, domain-specific platforms (e.g. DSP, ASIP) are optimized for a range of applications.
  Signal processing, cryptography, networking