## Slide 1: System-on-Chip Design
Hao Zheng
Comp Sci & Eng
U of South Florida

## Slide 2: Overview
A system-on-chip (SoC): a computing system on a single silicon substrate that integrates both hardware and software.
Hardware packages all necessary electronics for a particular application.
  which implemented by SW running on HW.
Aim for low power and low cost.
  Also more reliable than multi-component sys.

## Slide 3: SoC Hardware Architecture
Often used in embedded application.
How to implement an application on a HW platform executing some SW programs?
source: wiki

## Slide 4: Topics
Computational models for HW & SW
System modeling using SystemC
HW/SW partitioning
HW/SW interfacing
High-level synthesis
  Transforming SW to HW implementation
On-chip communication architectures
FPGA prototying, if time allows.

## Slide 5: Prerequisites
Working knowledge of C/C++ programming
Solid background in digital logic design
Good understanding of computer organization and architecture

## Slide 6: Textbooks
No required textbooks.
References:

## Slide 7: Evaluation
6-8 assignments: 60% of final grade
1 final project: 40% of final grade
Final grading scale
Need verifiable proof to make up missing/late assignments

## Slide 8: Course Communication
Course site on Canvas @ my.usf.edu
  Download assignments & submit your solutions
  Participate discussions
  Checking grades
www.cse.usf.edu/~zheng/teaching/soc
  Lecture slides
  reading assignments
  Other related material

## Slide 9: Embedded Systems
A computing device embedded in a larger system.
Pervasive
98% processors sold annually are used in embedded applications.

## Slide 10: Embedded Systems

## Slide 11: Embedded Systems: Design Challenges
Power/energy efficient: mobile & battery powered
Highly reliable: Extreme environment (e.g. temperature)
Real-time operations: predictable performance
Highly complex
  E.g. Mercedes Benz E-class
  55 electronic control units
  5 communication busses
Tightly coupled Software & Hardware
Rapid development at low price

## Slide 12: Design Complexity Challenges

## Slide 13: Design Complexity Challenges
Answer to design complexity challenges:
Move to higher levels of abstraction

## Slide 14: Levels of Abstraction: Behavior
Different levels of abstraction represent different modeling details

## Slide 15: Levels of Abstraction: Behavior

## Slide 16: Levels of Abstraction: Structure
Circuit: network of transistors
Logic: network of basic logic gates
  AND/OR/NOT, latches/FFs, etc.
Processor: network of logic components
  i.e. ALU, MUX, decoders, registers, etc.
  See Figure 1.5 in the Embedded book.
System: network of processors, memories, buses, and other custom processing logic.
    See Figure 1.8 in the Embedded book.

## Slide 17: System Behavioral Models
Multiple communicating concurrent processes for HW & SW.
Communication and synchronization.
Embedded book

## Slide 18: System Structural Models
Embedded book

## Slide 19: SoC Design Flow: A Simplified View
System Specification
HW/SW Partitioning
HW Model
SW Program
Synthesis
Compilation
HW/SW
Co-Verification
System Integration
HW Implementation
Binary Image
Exploration/
Estimation
CPU
Mem
HW
Impl.
IF
Read: section 2.6 – 2.7, Embedded book.

## Slide 20: Models of Computation
Formal abstract representations of a system
  various degrees of
    expressive power
    complexity
    Supported features
Examples
  HW: FSM, FSMD, super-state FSMD,
  SW: data flow, control flow, control-data flow, process network,

## Slide 21: System Specification: Language Requirements
Formality: formal syntax and semantics
Executability: validation through simulation
Synthesizability:
  Implementation in HW and/or SW
  Support for IP reuse
Modularity
  Hierarchical composition
  Separation of concepts
Simplicity

## Slide 22: System-Level Description Languages

## Slide 23: Synthesis
Converting a behavioral description to a structural one.
RTL synthesis is well known.
  Cycle accurate model -> logic gate netlist
High-level synthesis: from C to a structural model.
  Still in early stage of adoption.
System synthesis: system behavioral model -> system structural model
  under active research.

## Slide 24: System Synthesis
Processes -> CPUs or custom logic
  HW/SW partitioning
Communication -> Buses or NoC
Flow
  Profiling & Estimation
  Component & connection allocation
  Process and channel binding
  Process scheduling
  IF component insertion
  Model refinement

## Slide 25: Hardware/Software Co-Design
Definition: HW/SW co-design is the design of cooperating HW components and SW components in a single design effort.
Alternative definition:
HW/SW co-design means meeting system level objectives by exploiting the synergy of HW and SW through concurrent design.

## Slide 26: High-Level Synthesis
Embedded book

## Slide 27: Concurrency vs Parallelism
Concurrency: independent operations are arranged such that they may be executed simultaneously.
  Simultaneous executions may not be possible.
Parallelism: HW platform can execute multiple operations simultaneously.
  Parallelism is useless if SW does not display concurrency.

## Slide 28
System Design Methodology
The Embedded Book, Chapter 2

## Slide 29: Terminologies
+
A
B
Cin
S
Cout
Specification
Structural Model
Transistor level model
Implementation

## Slide 30: Historical Overview
Embedded
book

## Slide 31: Bottom-Up Methodology
Embedded book

## Slide 32: Top-Down Methodology
Embedded book

## Slide 33: Meet-in-the-Middle Methodology
Embedded book

## Slide 34: Platform Methodology
Reuse of previous defined platforms
  With well-defined structures and standard components.
Add more components necessary for an application.
  These components are then synthesized.
System implementation is generated by combining the layouts of existing and custom components.
Advantages: faster development, lower cost,

## Slide 35: An Example Platform: Xilinx Zynq

## Slide 36: Reading Guide
Embedded Book
  Chapter 1, sec 1.1 – 1.5, skip 1.3.1 – 1.3.2
  Chapter 2, skip 2.5
CoDesign Book
  Chapter 1

## Slide 37
Backup

## Slide 38: A System Level HW Design Flow